## Slide 1: Android Bluetooth-BSP part
Tungnt58

## Slide 2: Content
Android Bluetooth Architecture
Bluetooth Workflow
HIDL and Vendor Implementation

## Slide 3: Android Bluetooth Architecture
APPLICATION FRAMEWORK
Apps
Android.bluetooth
APPLICATION FRAMEWORK
Bluetooth Service
Packages/apps/Bluetooth
Bluetooth Profiles
JNI
Packages/apps/Bluetooth/jni
HIDL INTERFACES
hardware/interfaces/Bluetooth
Vendor Implement
Bluetooth Controller
BLUETOOTH STACK
system/bt
Bluetooth App layer
Bluetooth embedded system
HIDL
Binder
At the application framework level is application code, which uses the android.bluetooth APIs to interact with the Bluetooth hardware. Internally, this code calls the Bluetooth process through the Binder IPC mechanism.
Application Framework
The Bluetooth system service is package as an Android app and implements the Bluetooth services and profiles at the Android framework layer. This app calls into the native Bluetooth stack via JNI
Bluetooth system service
The JNI code calls into the Bluetooth stack when certain Bluetooth operations occur, such as when devices are discovered.
JNI
The stack implements the generic Bluetooth HAL and customizes it with extensions and configuration changes.
Bluetooth stack
Vendor devices interact with Bluetooth stack using the HIDL
Vendor implementation
Ref: https://source.android.com/docs/core/connect/bluetooth

## Slide 4: Android Bluetooth Architecture
APPLICATION FRAMEWORK
Apps
Android.bluetooth
APPLICATION FRAMEWORK
Bluetooth Service
Packages/apps/Bluetooth
Bluetooth Profiles
JNI
Packages/apps/Bluetooth/jni
HIDL INTERFACES
hardware/interfaces/Bluetooth
Vendor Implement
Bluetooth Controller
BLUETOOTH STACK
system/bt
Bluetooth App layer
Bluetooth embedded system
HIDL
Binder
BlueDroid
Bluetooth
AV(audio/video)
HF
PAN
…
BTIF
Bluetooth
AV(audio/video)
HF
PAN
…
BTA
BTM
BTU
L2CAP
HCI
…
Stack
BlueDroid Overview
BTIF (Bluetooth Interface): Provide Blueroid external interface
BTU (Bluetooth Upper Layer): undertake BTA and HCI
BTM (Bluetooth Manager): Bluetooth paring and link management
BTE (Bluetooth Embedded System):The internal processing of Bluedroid, subdivided into BTU, BTM and HCI
BTA (Bluetooth Application Layer): Logic implementation and processing of each profile
HCI (Host controller interface: Read/Write data to Bluetooth HW

## Slide 5: Bluetooth Workflow
Ref: https://blog.csdn.net/edmond999/article/details/115728286
Focus
HIDL INTERFACES
hardware/interfaces/Bluetooth
Vendor Implement
Bluetooth Controller
BLUETOOTH STACK
system/bt
Bluetooth App layer
Bluetooth embedded system
HIDL

## Slide 7: HIDL and Vendor Implementation
HIDL INTERFACES
hardware/interfaces/Bluetooth
Vendor Implement
Bluetooth Controller
BLUETOOTH STACK
system/bt
Bluetooth App layer
Bluetooth embedded system
HIDL
Transmit data
Receive data
HCI Layer (system/bt/hci)
Initialize {hci_initialize()}
Transmit data {hci_transmit()}
Receive ACL data
Receive SCO data
Send HCI command
Send ACL data
Send SCO data
HCI event receive
HIDL Layer(hardware/interfaces/bluetooth/)
Initialize {initialize(callbacks)}
Callback funcs {IBluetoothHciCallbacks interface}
Receive ACL data
Receive SCO data
Send HCI command
Send ACL data
Send SCO data
HCI event receive
Vendor Implementation
Bluetooth Hardware
write(fd…)
read(fd…)
Initialize {Initialize()}

## Slide 8: HCI Layer - Initialize
Initialize {hci_initialize()}
Back
System/bt/hci/src/hci_layer_android.cc

## Slide 9: HCI Layer – Transmit data
Back
Transmit data {hci_transmit()}
System/bt/hci/src/hci_layer_android.cc
ACL (Asynchronous Connection Less) for general data frame
SCO (Synchronous Connection Oriented) for synchronous audio frame

## Slide 10: HIDL Layer– Initialize
Back
Initialize {initialize(callbacks)}
hardware/interfaces/bluetooth/1.0/default/bluetooth_hci.cc

## Slide 11: HIDL Layer – IBluetoothHciCallbacks
Back
Callback funcs {IBluetoothHciCallbacks interface}
hardware/interfaces/bluetooth/1.0/IBluetoothHciCallbacks.hal

## Slide 12: HIDL Layer– Send data
Send data/command
Back
hardware/interfaces/bluetooth/1.0/default/bluetooth_hci.cc
hardware/interfaces/bluetooth/1.0/default/hci_internals.h

## Slide 13: Vendor Implementation
Send data via socket
Send data via UART device file
Method 1
Method 2
Vendor Implementation
Initialize {Initialize()}
write(fd…)
read(fd…)
Bluetooth Hardware
Kernel space
System call (socket()- hci interface)
Devfs (dev/tty*)
User
space
HCI driver
Network
stack
write(fd…)
read(fd…)
UART driver
rfkill driver
rfkill driver
Socket layer
net/Bluetooth/af_Bluetooth.c
transport layer
net/Bluetooth/hci_core.c
/dev/rfkill
sysfs/rfkill
/dev/rfkill
sysfs/rfkill
Libbt-vendor
dlopen(libbt-vendor.so)
Socket buffer
(struct sk_buff)
Vendor_interface.cc
Initialize {Initialize()}
UART driver
Back

## Slide 14: Vendor Implementation-Send data via socket
Back
Send data via socket
Vendor Implementation
Initialize {Initialize()}
write(fd…)
read(fd…)
Bluetooth Hardware
Kernel space
System call (socket()- hci interface)
User
space
HCI driver
Network
stack
rfkill driver
Socket layer
net/Bluetooth/af_Bluetooth.c
transport layer
net/Bluetooth/hci_core.c
/dev/rfkill
sysfs/rfkill
Socket buffer
(struct sk_buff)
UART driver

## Slide 15: Vendor Implementation-Send data via socket
User space vendor implementation
Initialize
Power on Bluetooth device
Open socket
Initialize Callback
Send data
sendHciCommand
sendAclData
sendScoData
system/bt/vendor_libs/linux/interface/bluetooth_hci.cc

## Slide 16: Vendor Implementation-Send data via socket
User space vendor implementation
Initialize
Power on Bluetooth device
Open socket
Initialize Callback
Send data
sendHciCommand
sendAclData
sendScoData
system/bt/vendor_libs/linux/interface/bluetooth_hci.cc

## Slide 17: Vendor Implementation-Send data via socket
User space vendor implementation
Initialize
Power on Bluetooth device
Open socket
Initialize Callback
Send data
sendHciCommand
sendAclData
sendScoData
system/bt/vendor_libs/linux/interface/bluetooth_hci.cc
system/bt/vendor_libs/linux/interface/async_fd_watcher.cc

## Slide 18: Vendor Implementation-Send data via socket
User space vendor implementation
Initialize
Power on Bluetooth device
Open socket
Initialize Callback
Send data
sendHciCommand
sendAclData
sendScoData
system/bt/vendor_libs/linux/interface/h4_protocol.cc
system/bt/vendor_libs/linux/interface/bluetooth_hci.cc
Back

## Slide 19: Vendor Implementation-HCI Driver
Back
HCI driver
Socket buffer
(struct sk_buff)
Bluetooth Hardware
hci_uart_open
hci_uart_close
hci_uart_send_frame
hci_uart_setup
hci_uart_receive_buf
HCI device
Serial device
Serdev RX buffer
Serdev TX buffer
serdev_device_write_buf
Send data
receive data
2. Register hci device
1. Register serial device driver
receive_buf
h4_recv_buf
hci_uart_write_work

## Slide 20: Vendor Implementation-HCI Driver
Back
1. Register serial device driver
https://github.com/torvalds/linux/blob/master/drivers/bluetooth/hci_nokia.c

## Slide 21: Vendor Implementation-HCI Driver
Back
2. Register hci device

## Slide 22: Vendor Implementation-HCI Driver
Back
hci_uart_send_frame() workflow
Start write data

## Slide 23: Vendor Implementation-HCI Driver
Back
hci_uart_receive_buf() workflow

## Slide 24: Vendor Implementation-Send data via UART device file
Back
Send data via UART device file
Vendor Implementation
Bluetooth Hardware
Kernel space
User
space
Devfs (dev/tty*)
write(fd…)
read(fd…)
UART driver
rfkill driver
/dev/rfkill
sysfs/rfkill
Libbt-vendor
dlopen(libbt-vendor.so)
Vendor_interface.cc
Initialize {Initialize()}

## Slide 25: Vendor Implementation-Send data via UART device file
Libbt-vendor
Initialize {init()}
Vendor specific operation {*op()}
Cleanup()
Create dynamic library entry point
hardware/broadcom/libbt/src/bt_vendor_brcm.c
hardware/broadcom/libbt/include/vnd_anthias.txt
hardware/interfaces/bluetooth/1.0/default/bt_vendor_lib.h

## Slide 26: Vendor Implementation-Send data via UART device file
Libbt-vendor
Initialize {init()}
Vendor specific operation {*op()}
Cleanup()
Create dynamic library entry point
hardware/broadcom/libbt/src/bt_vendor_brcm.c

## Slide 27: Vendor Implementation-Send data via UART device file
Libbt-vendor
Initialize {init()}
Vendor specific operation {*op()}
Cleanup()
Create dynamic library entry point
hardware/broadcom/libbt/src/bt_vendor_brcm.c

## Slide 28: Vendor Implementation-Send data via UART device file
Libbt-vendor
Initialize {init()}
Vendor specific operation {*op()}
Cleanup()
Create dynamic library entry point
hardware/broadcom/libbt/src/bt_vendor_brcm.c
hardware/broadcom/libbt/src/userial_vendor.c

## Slide 29: Vendor Implementation-Send data via UART device file
Back
Libbt-vendor
Initialize {init()}
Vendor specific operation {*op()}
Cleanup()
Create dynamic library entry point
hardware/broadcom/libbt/src/bt_vendor_brcm.c
hardware/broadcom/libbt/src/upio.c

## Slide 30: Vendor Implementation-Send data via UART device file
Vendor_interface.cc
Initialize {init()}
Send data functions
hardware/broadcom/libbt/src/bt_vendor_brcm.c
hardware/broadcom/libbt/src/userial_vendor.c

## Slide 31: Vendor Implementation-Send data via UART device file
Vendor_interface.cc
Initialize {init()}
Send data functions
hardware/interfaces/bluetooth/1.0/default/vendor_interface.cc
hardware/interfaces/bluetooth/1.0/default/h4_protocol.cc
Back

## Slide 32
THANKS